## Slide 1: NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu Computer Architecture Research Lab
http://arch.cse.ohio-state.edu

## Slide 2: Outline
Motivation
NVSleep Framework Design
NVSleep Implementation
Evaluation
Conclusion
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 3
Idle/leakage power: source of inefficiency in CMPs
  Expected to increase in future technologies
Cores are often idle, wasting power
Power gating can help
  Functional units with little or no states (ALUs) – power gating OK
  Most FUs have significant states (RF, ROB, …) – power gating expensive
NVSleep Idea: non-volatile memory can enable fast micro-checkpointing
  Reduce the performance overhead of power gating
  Enable power gating during short idle intervals (e.g. stalls on LLC misses)
Motivation
Chart: Idle Power Breakdown
| Idle (30%) | Active (70%)
Idle Power Breakdown | 0.30389 | 0.69611
Shimpi et al., The Haswell Review: Intel Core i7-4770K & i5-4670K Tested, www.anandtech.com
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 4
We use Spin Transfer Torque RAM, a new type of magnetic memory
STT-RAM can be a good candidate for NVSleep checkpointing
STT-RAM has other good characteristics:
  ~4X higher density than SRAM, better scalability
  Infinite write endurance
STT-RAM in NVSleep
NVSleep checkpointing
Non-volatility
Low latency access
Low energy
STT-RAM
Long data retention time (as long as 10 years)
Fast read (~0.9X SRAM)
Low energy read (~0.7X SRAM)



NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu
and slow write (~ 20X SRAM)
and high energy write
(~20X SRAM)

## Slide 5: Outline
Motivation
NVSleep Framework Design
NVSleep Implementation
Evaluation
Conclusion
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 6
NVSleep leverages STT-RAM for on-chip storage structures
  Write latency-tolerant units (caches, TLBs, etc.) are implemented with STT-RAM (combined with SRAM write buffers to help hide long latency writes)
  Write latency-sensitive units (RF, ROB, etc.) are implemented with hybrid SRAM/STT-RAM design
NVSleep Framework
Execution Cluster
Caches, TLBs, etc.
RF, ROB, etc.
Core
STT-RAM
SRAM
CMOS
SHTDWN
WAKEUP
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 7
SRAM/STT-RAM hybrid Design
SRAM for primary storage
STT-RAM shadow of identical size used for micro-checkpointing
Banked design to parallelize checkpointing process
SRAM Master
STT-RAM Shadow
bank 0
bank 1
bank 2
bank 3
checkpoint control
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 8: Outline
Motivation
NVSleep Framework Design
NVSleep Implementation
Evaluation
Conclusion
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 9
NVSleepMiss: Hardware-driven
  Ideal for short idle events, detected by hardware
  Our implementation: cores sleep on LLC misses
NVSleepBarrier: Software API
  Exposes NVSleep to the system software
  Can be used by the OS or applications to “suspend” cores quickly
  Ideal for software observable idle events such as blocking on synchronization (e.g. barriers, locks, etc.)
  Our implementation: cores sleep when blocked on barriers
NVSleep Implementation
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 10
  LD issued, missed in L1
  LLC miss reported by LLC
  Sleep signal sent to Core 0
  Checkpointing starts
  Core 0 goes to sleep after stalls
  Missing data returns
  Wakeup signal sent to Core 0
NVSleepMiss: Hardware-driven
Core 0
L1
0x00FF
CTRL
MSHR
Core N
L1
CTRL
L2
Cache
…
…
1
2
3
6
7
LD(0x00FF)
LLCMiss(0x00FF)
SHTDWN
Data(0x00FF)
WAKEUP
Checkpointing and wakeup of cores are coordinated by the L1 cache controller of each core
Hardware-driven checkpointing/wakeup sequence:
4
CKP
5
Sleep
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 11
  Expose micro-checkpointing system to software through API
    Dedicated sleep(0xADDR) instruction
    When executed on a core – it will shut down
    Wakeup triggered by another core through write operation to 0xADDR
NVSleepBarrier: Software API
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu
  Example application in barrier:
    All but last thread – sleep(&sense)
    Last thread writes to sense, wakes-up all other threads
void barrier(int count, int sense, int num_threads)
{
int local_sense;
local_sense = !sense;
if (count != (num_threads - 1)) {
while (local_sense != sense) {
sleep(&sense);
}
}
else {
count = 0;
sense = local_sense;
}
}

## Slide 12
  Software-driven checkpointing/wakeup sequence:
NVSleepBarrier: Software API
L2
Cache
…
…
Core N
L1
CTRL
3
ST(&sense)
4
5
INV(&sense)
WAKEUP
  sleep(&sense) executed by Core 0
  “&sense” reserved in Core 0 L1
  write(&sense) executed by Core N
  Coherence: invalidate(&sense)
  Wakeup signal sent to all cores
Core 0
L1
CTRL
1
2
sleep(&sense)
Core 1
L1
CTRL
&sense
r
&sense
r
&sense
w
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 13: Outline
Motivation
NVSleep Framework Design
NVSleep Implementation
Evaluation
Conclusion
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 14
  Simulation Framework:
    SESC for architecture simulation
    CACTI, McPAT, and NVSim for power, energy, and area simulation
  Benchmarks:
    Single-threaded: SPEC CPU2000
    Multi-threaded: SPLASH2 and PARSEC
  Main Evaluated Configuration:
    CMP with 64 out of order cores
Methodology
      8-bank design SRAM/STT-RAM hybrid structures
      3.3ns STT-RAM write latency for checkpointing
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 15
  NVSleepMiss: 23% (SPECFP) and 17% (SPECINT) energy reduction
NVSleepMiss Energy Reduction
Chart: SPEC Integer Benchmarks
| bzip2 | crafty | gap | gzip | mcf | parser | twolf | vortex | GeoMean
SRAM Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
NVNoSleep | 0.92699 | 0.91912 | 0.92201 | 0.90477 | 0.8391 | 0.89685 | 0.90039 | 0.92656 | 0.90406
NVSleepMiss | 0.92369 | 0.91659 | 0.88929 | 0.89897 | 0.46462 | 0.84638 | 0.89778 | 0.92528 | 0.82808
NVSleepIdeal | 0.92187 | 0.91531 | 0.87499 | 0.89556 | 0.37238 | 0.83532 | 0.89694 | 0.92355 | 0.80154
Chart: SPEC FP Benchmarks
| art | ammp | applu | apsi | equake | mgrid | sixtrack | swim | wupwise | GeoMean
SRAM Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
NVNoSleep | 0.88314 | 0.91667 | 0.93011 | 0.91563 | 0.87294 | 0.88764 | 0.92687 | 0.86745 | 0.91141 | 0.90104
NVSleepMiss | 0.78538 | 0.83771 | 0.89587 | 0.87379 | 0.60901 | 0.62629 | 0.91932 | 0.66158 | 0.77303 | 0.76746
NVSleepIdeal | 0.68023 | 0.82671 | 0.87076 | 0.85063 | 0.49485 | 0.55819 | 0.91388 | 0.52839 | 0.70226 | 0.69738
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu
10%
23%
30%

## Slide 16
NVSleepBarrier Energy Reduction
NVSleepBarrier: 34% energy reduction for apps with >10 barriers
Chart: Multithreaded Apps with Low Barrier Count (<10)
| blackscholes | dedup | swaptions | cholesky | fft | raytrace | GeoMean
SRAM Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1
NVNoSleep | 0.90679 | 0.77748 | 0.91365 | 0.89262 | 0.85462 | 0.89267 | 0.87167
NVSleepMiss | 0.90409 | 0.76529 | 0.90249 | 0.88671 | 0.82066 | 0.83622 | 0.85105
NVSleepBarrier | 0.90929 | 0.77748 | 0.91365 | 0.86727 | 0.81234 | 0.8799 | 0.85852
NVSleepCombined | 0.90487 | 0.76529 | 0.90249 | 0.81917 | 0.77233 | 0.84137 | 0.83241
Chart: Multithreaded Apps with High Barrier Count (>10)
| bodytrack | fluidanimate | streamcluster | barnes | lu | ocean | radiosity | radix | water-nsquared | GeoMean
SRAM Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
NVNoSleep | 0.88631 | 0.75376 | 0.8872 | 0.91146 | 0.89191 | 0.82818 | 0.88331 | 0.83076 | 0.87975 | 0.86011
NVSleepMiss | 0.88896 | 0.74803 | 0.88648 | 0.90602 | 0.89175 | 0.80657 | 0.88279 | 0.81987 | 0.86421 | 0.85347
NVSleepBarrier | 0.8481 | 0.608 | 0.77899 | 0.84532 | 0.16163 | 0.78351 | 0.87478 | 0.79204 | 0.82239 | 0.66225
NVSleepCombined | 0.8498 | 0.60139 | 0.77905 | 0.83854 | 0.16142 | 0.76252 | 0.86238 | 0.7795 | 0.81002 | 0.6556
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 17
Sensitivity Studies
Chart: Multithreaded Apps with High Barrier Count (>10)
| 16 cores | 32 cores | 64 cores
SRAM Baseline | 1 | 1 | 1
NVSleepMiss | 0.86688 | 0.85588 | 0.85347
NVSleepBarrier | 0.75982 | 0.70757 | 0.66225
NVSleepCombined | 0.74649 | 0.69635 | 0.6556
Chart: STT-RAM Write Latency (ns)
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
NVNoSleep | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
NVSleepMiss | 0.8603 | 0.87599 | 0.89211 | 0.90791 | 0.92338 | 0.93852 | 0.95335 | 0.9679 | 0.98218 | 0.99621 | 1.01 | 1.0236
NVSleepBarrier | 0.84938 | 0.84958 | 0.84979 | 0.85 | 0.8502 | 0.85041 | 0.85061 | 0.85081 | 0.85102 | 0.85122 | 0.85142 | 0.85162
Num of Banks | energy/access (pJ) | area (mm2)
1 | 0.448 | 0.007543
2 | 0.552 | 0.012091
4 | 0.628 | 0.018883
8 | 0.741 | 0.029032
Chart: SPEC Benchmarks
| 1-bank | 2-bank | 4-bank | 8-bank
SRAM Baseline | 1 | 1 | 1 | 1
NVNoSleep | 0.88982 | 0.89429 | 0.8976 | 0.90246
NVSleepMiss | 1.0629 | 0.9196 | 0.8377 | 0.79541
More details can be found in the paper!
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 18
Conclusion
  The first work to use non-volatility feature of STT-RAM to implement pipeline-level checkpointing
  A general and low overhead framework for reducing energy through exploiting short idle execution phases
  Achieved energy reduction of 17-34% with less than 3% performance and area overheads
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 19
Questions?
Thank you!
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 20
Backup Slides
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 21
NVSleep MSHR Design
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 22
Core Idle Time Analysis
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 23
Performance Overhead
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu

## Slide 24
Area Overhead
  Area – less than 3% compared to SRAM baseline
    STT-RAM shadow structures increase area
    STT-RAM caches help decrease area
NVSleep: Using Non-Volatile Memory to Enable Fast Sleep/Wakeup of Idle Cores
Xiang Pan and Radu Teodorescu